1966 Fender Showman Amp AB763 Maintenance Log Riley McDowell

February 2020
- Amp purchased from Reverb.com shipping from Portland OR - $725
- Works, but has moderate 60Hz hum with 120Hz overtone
- Missing Fender logo and tube chart
- Incorrect
  - Fuse rating (was 10A)
  - Front baffle (too thick, non-fender grille cloth)
  - One B+ filter capacitor found installed with reverse polarity
  - PI tube is 12AX7 instead of 12AT7
- Inspection reveals
  - Plate shorted to heater in past
    - Center tap of power transformer heater winding overheated
      - Burned all cloth insulation from center tap wire
    - 470 Ohm grid resistor discolored, reading ~600 Ohms
  - Oily wiring & green rust on some cloth wiring – potentially conductive?
  - Power tubes mismatched, but not bad enough to swap out
March-April 2020
- Replaced power transformer with ClassicTone model 40-18004, sold as drop-in replacement
- It was not a drop-in replacement. Negative bias circuit was -60VAC instead of original -48VAC, requiring modification to bias circuit to achieve rated power dissipation
  - Bias resistors modified to allow setting appropriate bias voltage
    - 680 Ohm, 22k Ohm, 4.7k Ohm and 3.3m Ohm as seen in schematic
- Amp still has 60Hz/120Hz hum
  - Added star grounding
  - Modified to Fender Twin Reverb ‘65 Reissue specs
    - 2x 220uF B+ filter caps
    - 100uF 100V bias supply filter cap
    - Additional 22uF 100V adjusted bias filter cap
    - Phase inverter input coupling cap doubled to 0.001uF
  - Replaced all remaining electrolytic capacitors
  - Replaced eyelet board with non-conductive reproduction
  - Replaced resistors with excessive drift
  - Replaced oscillator disk capacitors
  - Replaced PI output coupling caps
  - Replace volume/tone pots and associated wiring
  - Shielded input to first gain stages
  - Grounded PI stage directly to output speaker jack
- 1 Ohm precision bias measurement resistors mounted to electrically isolated standoffs
- Replacement grounded convenience outlet
- Replacement metal/rubber feet
- New grille cloth and baffle board
- Replacement Fender logo
- Custom replacement tube chart https://github.com/rileymcdowell/showman